## Slide 1
IFORD
Geospatial Data
with R
Day 3_Day4 — Raster Data in R. [Mastering Raster Data & Spatial Algebra]
Agenda for the day: raster objects on their own, then combining them with vector objects.

## Slide 2
DAILY SCHEDULE
Strategic Objectives for the Day
A two-part approach, as on the previous day
PART 1
Raster Objects Alone
Internal structure of a raster: pixels, bands, resolution, extent. Critical transition from raster to Terra. Reading satellite rasters and operations applicable to rasters alone.
PART 2
Raster + Vector
Overlaying administrative polygons on the pixel grid. Extracting area statistics. Case study: SRTM DTM and land cover in Cameroon.
Expected outcome: a reproducible R script covering the entire process from importing the raw raster to generating decision-making indicators by administrative unit.
Slide 2
IFORD — R Geospatial · Day 3

## Slide 3
PART 1
Raster Objects Alone
Structure, packages, and operations that apply to the raster independently of any vector data

## Slide 4
PART 1 · KEY CONCEPTS
Anatomy of Matrix Data
▭
Extent
Boundary coordinates (Xmin, Xmax, Ymin, Ymax) defining the bounding box of the study area.
◱
Spatial resolution
Actual ground size of a pixel (e.g., 30 m for SRTM). Determines the level of detail in the analysis.
▤
Bands
Single-channel (elevation) or multiband (multispectral satellite imagery) rasters.
⊕
CRS
Coordinate Reference System. Crucial for georeferencing. Standardized to WGS 84 (EPSG:4326).
Slide 4
IFORD — R Geospatial · Day 3

## Slide 5
PART 1 · ARCHITECTURE
Technological Evolution: From Raster to Terra
Criteria | Raster Package (Legacy) | Terra package (standard)
Implementation | R, heavy dependencies | Native C++
Performance | Historical Reference | Up to 50x faster
Memory | Large-scale bottlenecks | Maximum RAM optimization, nationwide scale
Key Classes | RasterLayer / Stack / Brick | SpatRaster · SpatVector
Recommendation: All new analyses should be developed using terra. The raster package is mentioned here only for the purpose of reading legacy scripts.
Slide 5
IFORD — R Geospatial · Day 3

## Slide 6
PART 1 · DATA READING
Reading Satellite-Derived Rasters
library(terra)
# Single-band raster (e.g., SRTM DTM)
mnt <- rast("srtm_cameroun.tif")
# Multiband raster (e.g., Copernicus)
landcover <- rast("copernicus_lc.tif")
# Inspecting the structure
crs(mnt); res(mnt); ext(mnt); nlyr(mnt)
▲
SRTM DTM
Topography — 30 m resolution
▦
Copernicus Land Cover
Land cover — 100 m resolution
Slide 6
IFORD — R Geospatial · Day 3

## Slide 7
PART 1 · GEOTECHNICAL ENGINEERING
Cutting and Masking
1
Cropping — crop()
Crops the matrix to the rectangular bounding box of the study area.
mnt_crop <-
crop(mnt, extent)
2
Masking — mask()
Sets any pixel located outside the exact administrative boundaries to NA.
mnt_msk <-
mask(mnt_crop, boundary)
Institutional Rigor
These operations ensure that your statistics apply only to the sovereign territory, eliminating peripheral noise and streamlining calculations.
Slide 7
IFORD — R Geospatial · Day 3

## Slide 8
PART 1 · GEOPROCESSING
Resampling and Aggregation
resample()
Aligns a source raster to the geometry of a target raster. This step is required before performing any map algebra operations.
aggregate()
Reduces the resolution to produce larger cells. Uses mean (physical variable) or sum (counting variable).
Interpolation Semantics
near — for categorical variables (land cover).
bilinear — for continuous variables (topography, temperature).
⚠ Common pitfall: Using `mean` for a stock variable (population) underestimates the totals—use `sum` instead.
Slide 8
IFORD — R Geospatial · Day 3

## Slide 9
PART 2
Raster + Vector Combination
The intersection between the physical world (raster) and the administrative world (vectors)

## Slide 10
PART 2 · PIVOT ANALYSIS
Area Statistics — extract()
vect_reg <- vect("gadm41_CMR_1.shp")
stats <- extract(mnt_msk, vect_reg,
fun = mean, na.rm = TRUE)
Decision-Making Applications
•
Overlays the official polygons onto the pixel grid.
•
Captures all intersecting cells.
•
Generates consolidated decision-making indicators by region or department.
“This is the point where the physical world (raster) and the political world (administrative vectors) converge.”
Slide 10
IFORD — R Geospatial · Day 3

## Slide 11
PART 2 · SCHOOL CASE STUDY
Case Study: Risks in Cameroon
!
Urban Vulnerabilities
Identify built-up areas located in low-lying areas that are prone to flooding.
Risk = (Elevation < 500 m)
& (Urban == 3)
Note: Code 3 corresponds to the “Urban” class in Copernicus Land Cover.
Layer | Source | Resolution
srtm_cameroun.tif | SRTM (NASA/USGS) | 30 m
copernicus_lc.tif | Copernicus GLC | 100 m
gadm41_CMR_1.shp | GADM Level 1 | vector
Cross-sectoral application
The integration of topography (SRTM) and land cover (Copernicus) transforms two physical layers into a risk indicator that can be directly used for public decision-making.
Slide 11
IFORD — R Geospatial · Day 3

## Slide 12
R PRODUCTION SYNTAX
Complete Algebraic Implementation
library(terra)
# 1. Importing data structures — [Part 1: Raster only]
srtm_cmr <- rast("srtm_cameroun.tif")
vect_reg <- vect("gadm41_CMR_1.shp")
# 2. Alignment and masking — [Part 1: Raster only]
srtm_msk <- mask(crop(srtm_cmr, vect_reg), vect_reg)
# 3. Multicriteria map algebra — [Part 2: raster + vector]
zones_risk <- (srtm_msk < 500) & (landcover == 3)
# 4. Extraction by GADM unit — [Part 2: raster + vector]
stats <- terra::extract(srtm_msk, vect_reg, fun = mean, na.rm = TRUE)
Slide 12
IFORD — R Geospatial · Day 3

## Slide 13
SUMMARY
Spatial Statistician’s Checklist
1
CRS Alert
Verify that the coordinate systems are exactly the same before any extract() operation.
2
RAM Footprint
Always include `crop()` at the beginning to reduce the size of the matrices.
3
NA Caution
The argument na.rm = TRUE is required for valid official figures.
Slide 13
IFORD — R Geospatial · Day 3

## Slide 14
END OF THE SESSION — DAY 3
IFORD — Excellence & Rigor
Raster only → Raster + vector → Decision.

## Slide 15
REFERENCES
Image Sources
Topographic cover illustration:
en-gb.topographic-map.com
Slide 15
IFORD — R Geospatial · Day 3